## Slide 1: AIR POLLUTION TODAY: Ozone and fine particulate matter (PM2.5) are the major pollutants
US EPA [2020], OECD [2012]
US population exposed to air pollutants
in excess of national ambient air quality standards (NAAQS), 2018
PM2.5
PM10
SO2
Lead
Ozone
CO
NO2
137M
31
38M
0
1M
3M
16M
0
70 ppb (8-h average)
12 µg m-3 (annual), 35 µg m-3 (24-h)
Million environmental deaths per year
worldwide
2010 data

## Slide 2
Ozone effect on crops
Many crops show decreased yield at ozone >40 ppb

## Slide 3
Ozone effect on trees
[EPA, 2014]
W126 metric: weighted seasonal dose of ozone in excess of 60 ppbv
proposed secondary standard:
W126 = 7-15 ppm h
W126, ppm h
Relative biomass loss
W126 ozone for 2006-2008

## Slide 4
0 20 40 60 80 100 120 ppb
Europe AQS
(seasonal)
U.S. AQS
(8-h avg.)
U.S. AQS
(1-h avg.)
Preindustrial
ozone
background
Present-day ozone background at northern mid-latitudes
Europe AQS
(8-h avg.)
Canadian AQS
(8-h avg.)
Ozone air quality standards in the US and in the world
2008
2014
1997
China AQS
(8-h avg.)

## Slide 5: Days per year exceeding 70 ppb ozone standard, 2010-2014
TOAR [2017]

## Slide 6: Very severe ozone pollution problem in China
Li et al. [2019a]
China
air quality standard
US
air quality standard
revealed by air quality network observations starting in 2013

## Slide 7: Controlling ozone pollution requires understanding of whether ozone production is NOx- or VOC-limited
This is because anthropogenic sources are different:
NOx is from fuel combustion
VOCs are from leaks, industry, domestic products

## Slide 8: Until 2000s, ozone production in US was thought to be VOC-limited…
VOC
NOx-limited regime
VOC-limited regime
Typical
anthropogenic
emission inventory
estimate
…motivating strategy of VOC emission controls

## Slide 9: 1970-2003 trend of US emissions
Focus until 2000s was on VOC controls,
but ozone was not decreasing except in
Los Angeles and New York. Why?
Fiore et al. [1998]
1980-1995 trend in summer ozone (ppb a-1)

## Slide 10: Emission of biogenic VOCs first quantified in late 1980s
Many, many compounds emitted as photosynthesis and metabolism by-products, insect attractors or repellents, response to stress and injury
Principal hydrocarbons are emitted as C5H8 units:
Isoprene (C5H8)
Terpenes (C10H16)
Limonene
Myrcene
α-pinene
β-pinene
Caryophyllene
Sesquiterpenes (C15H24)
50% of total biogenic VOCs
very reactive
Pat Zimmerman

## Slide 11: Most of US is NOx-limited due to high emissions of biogenic isoprene
OMI satellite observations of formaldehyde (HCHO) columns, May-Aug 2005-2014
HCHO
h , OH
oxidation
~ 1 hour
Zhu et al. [2017]
isoprene
~ 1 hour
Other VOCs

## Slide 13: But what this really means is that ozone production is NOx-limited
VOC
NOx-limited regime
VOC-limited regime
anthropogenic
emissions
…so emission controls should focus on NOx
+ biogenic emissions
total
emissions

## Slide 14: Rethinking the ozone problem (NRC, 1991)
Tells EPA that ozone is a regional pollution problem, advises NOx emission controls
John Seinfeld
Jennifer Logan

## Slide 15: US NOx emissions have decreased by 54% from 2000 to 2016
Chart: 
 | 8818.9369 | 942.9878 | 12560.4881 | 276.0208
2000
Power
39% plants
4% Industry
(non-power plant)
Mobile 56%
US EPA, National Emission Inventory (NEI) 2011
2016
Chart: 
 | 2775.5783 | 1400.796 | 6020.935 | 291.7175
13%
57%
26%
Notes: TRANSITION: in order to monitor these changes in surface emissions we look to satellite observations

## Slide 16: Evidence of NOx emission decrease from satellite NO2 data
OMI NO2, summer 2005
Russell et al. [2012]

## Slide 17: Evidence of NOx emission decrease from satellite NO2 data
OMI NO2, summer 2005
OMI NO2, summer 2011
30% decrease in NOx emissions from 2005 to 2011
Russell et al. [2012]

## Slide 18: Take it from the communicator-in-chief…

## Slide 19: Trend in #days/year with ozone > 70 ppb, summer 2000-2014
Megacity trends
Parrish [2014], TOAR [2017], Wang et al. [2017]

## Slide 20: Ozone production efficiency (OPE) per unit NOx emitted
HO2
OH
NO2
NO
HNO3
VOC
hv
O3
Emission
Deposition
OPE  as OH  and therefore as NOx  and VOC 
So the efficacy of NOx emission controls decreases as NOx decreases

## Slide 21: Ozone in China has been increasing despite Clean Air Action starting in 2013
Emission controls have been targeted (successfully!) at PM2.5
NOx emissions have decreased by 30% since 2013 while VOC emissions have stayed flat.

## Slide 22: Unlike in US, ozone production in China is VOC-limited
OMI annual mean tropospheric column data, 2006-2007
Glyoxal (CHOCHO) Formaldehyde (HCHO) NO2
(440-460 nm) (340-360 nm) (420-450 nm)
NOx emissions are very high and VOC emissions are largely anthropogenic
Chan Miller et al. [2016]

## Slide 23: Decrease in PM2.5 pollution may be responsible for increase in ozone
Model increase in ozone due to PM changes
2013-2017 decrease in PM2.5
increases radicals for ozone production
Li et al. [2019a]
Nitrogen oxides (NOx)
Organics (VOCs)
Ozone
Sunlight
HO2 radicals
particles
particles scavenge HO2 radicals that would otherwise produce ozone
H2O

## Slide 24: COVID-19 lockdown reveals fast wintertime ozone production in Beijing
As NOx emissions decrease during lockdown, ozone production surges
Formaldehyde from VOCs provides the main radical source:
Li et al., 2021
before Jan 24 after Jan 24
MDA8 ozone
in N China Plain
Beijing observations and model
TROPOMI NO2
TROPOMI HCHO
MDA8 ozone
PM2.5
PAN
Observations
Model

## Slide 25: NOx controls are needed to meet current ozone standards … even if production is locally VOC-limited
VOC
NOx-limited regime
VOC-limited regime
Biogenic VOC background
Natural NOx background
start point
NOx controls are only way to get to current ozone standards and have side benefits
(NO2 air quality, nitrogen deposition)
VOC controls will only get you so far until you are limited by biogenic background

## Slide 26: As ozone standard tightens, the nature of the problem changes
Seasonal dose in excess of 60 ppb [EPA, 2014]
60 ppb exceedances are largest in Intermountain West

## Slide 27: Ozone in Intermountain West originates out of N America
Background = ozone present in absence of anthropogenic sources in North America
Domestic emissions have little influence on intermountain west
Anthropogenic background contributes ~15 ppb with little day-to-day variability
Zhang et al. [2014]
Ozone over NE Pacific
(INTEX-B, Apr-May 2006)
observed
GEOS-Chem
Ozone, ppb
Altitude, km
downwelling
Mean profile over NE Pacific,
Apr-May 2006 (INTEX-B)
MDA8 ozone, ppb
2006
observed
GEOS-Chem model
GEOS-Chem natural
GEOS-Chem background
Pinedale, Wyoming
2.4 km altitude

## Slide 28: Intercontinental transport of ozone pollution
2012 OMI NO2 column, 1015 molecules cm-2
Ozone pollution transport (GEOS-Chem model)
Strong westerlies
transport ozone
around mid-latitudes
N America
Europe
Asia