## Slide 1
Why is ozone so high (and increasing) over Korea and China?
Daniel J. Jacob
Vasco McCoy Family Professor of Atmospheric Chemistry and Environmental Engineering
Harvard University
Nadia Colombi
Laura Yang
Shixian Zhai
Drew Pendergrass
Ellie Beaudry

## Slide 2: Atmospheric ozone: “good up high, bad nearby”
Troposphere
Stratosphere:
90% of total
00
O2 + hv → O + O
O + O2 + M → O3 + M
In stratosphere:
In troposphere:
NO2 + hv → NO + O
O + O2 + M → O3 + M
(catalytic mechanism)
tropopause
UV SHIELD
TOXIC

## Slide 3: First recorded photochemical smog event: Los Angeles on July 26, 1943
Visibility down to three city blocks
Air smells like bleach
Is this Japanese chemical warfare?
Los Angeles Times, July 27, 1943

## Slide 4: Haagen-Smit (1953) identifies ozone produced in air from car exhaust as the harmful component in Los Angeles smog
ozone
NO
VOCs, CO
Shows in the lab that ozone is produced by photochemical oxidation of volatile organic compounds (VOCs) and CO in the presence of nitric oxide (NO)
Arie Haagen-Smit
fuel (CxHy)
air
In car engine:
NO2
NO2 absorbs in the blue
hv

## Slide 5: Current US exceedances of air quality standards (AQS)
US EPA [2020]
US population (millions) exposed to air pollutants
in excess of national ambient air quality standards, 2018
PM2.5
PM10
SO2
Lead
Ozone
CO
NO2
137M
31
38M
0
1M
3M
16M
0
70 ppb (maximum daily 8-h average, MDA8)
One third of US population breathes unhealthy high-ozone air according to US EPA

## Slide 6: Days per year exceeding 70 ppb ozone standard, 2010-2014
TOAR [2020]
Korean AQS: 60 ppb
China AQS: 75 ppb

## Slide 7: Very severe ozone pollution problem in China
Li et al. [2019]
China
air quality standard
US
air quality standard
revealed by air quality network observations starting in 2013

## Slide 8: Ozone in China and Korea has been getting worse over past decade
Li et al. [2020],
Pendergrass et al. [2022], Colombi et al., in prep.

## Slide 9: Role of emissions in driving 2015-2019 ozone trend in Seoul
Use random forest algorithm to correct for effect of meteorology in driving the 2015-2019 trend
Meteorology-corrected trend confirms effect of emission changes
Largest increasing trend in spring, decrease in August
90th percentile MDA8 ozone for 79 sites
in Seoul metropolitan area
Colombi et al., in prep.

## Slide 10: High ozone over Korea and China due to high emissions of NOx and VOCs
NOx from fuel combustion
VOCs from leaks, industry, domestic products
NOx emissions have decreased while urban VOC emissions have increased
Satellite NO2
2011-2019
NO2 trend
2011-2019
Satellite HCHO
2011-2019
HCHO trend
2011-2019
Ahn et al., submitted

## Slide 11: How does ozone production depend on NOx and VOCs? Need to understand chain mechanism
Initiation: production of HOx radicals
hydrogen oxide radicals: HOx ≡ OH + HO2
nitrogen oxide radicals: NOx ≡ NO + NO2
Propagation: cycling of HOx and NOx radicals to produce ozone
Termination: loss of HOx radicals
Oxidation of VOCs and CO catalyzed by
(both in gas phase and in aerosol)

## Slide 12
O3
HO2
NO
H2O2
VOC
NO2
hn
hv, H2O
OH
HNO3
Dependence of ozone and OH on NOx and VOCs
HO2 in this diagram denotes the ensemble of peroxy radicals including RO2
View CO as just another VOC
Two distinct chemical regimes depending on the chain-terminating pathway
self, PM

## Slide 13: Dependence of ozone and OH on NOx and VOCs
O3
HO2
NO
H2O2
VOC
NO2
hn
OH
NOx-limited regime:
O3 ↑ as NOx↑ PM ↓
self, PM
hv, H2O

## Slide 14: Dependence of ozone and OH on NOx and VOCs
O3
HO2
NO
VOC
NO2
hn
OH
HNO3
VOC-limited regime:
O3 ↑ as VOCs↑ NOx↓
hv, H2O

## Slide 15: Dependence of ozone and OH on NOx and VOCs
O3
HO2
NO
H2O2
VOC
NO2
hn
OH
HNO3
NOx-limited regime
VOC-limited regime
O3
NOx
NOx-limited
VOC-limited
O3
NOx-limited
VOC-limited
VOCs
self, PM
hv, H2O
O3
PM
NOx-limited

## Slide 16: Ozone (ppb) vs. NOx and VOC emissions Generic model calculation
VOC
VOC-limited
regime
NOx-limited regime
Ridge
clean
air
Polluted air
Ozone production in clean air is NOx-limited
Ozone production in polluted air tends to be NOx-limited in summer, VOC-limited in other seasons
Decreasing PM could explain summertime ozone increase in China

## Slide 17: COVID-19 lockdown reveals fast wintertime ozone production in Beijing
Li et al., 2021
before Jan 24 after Jan 24
MDA8 ozone
in N China Plain
circles = observed, background = model
Beijing observations and model
TROPOMI satellite NO2
MDA8 ozone
PM2.5
PAN
Observations
Model
NOx emissions decreased by 70% during lockdown, causing ozone production to surge under strongly VOC-limited conditions
Formaldehyde from VOCs provides the main HOx radical source:

## Slide 18: Decreasing NOx emission in China drives ozone pollution spread to early spring
As NOx emissions decrease, ozone production under VOC-limited conditions increases
Very high VOC emissions in China drive high ozone pollution as early as March
Li et al. [2021]

## Slide 19: KORUS-AQ aircraft campaign targeted at air quality over Korea
AirKorea AQ network
Flight tracks, May-June 2016
Ozone, ppb
Stagnant period (May 17-22)
Transport from China period (May 24-31)
Models systematically underestimate ozone including the high-altitude background
Park et al. [2021]

## Slide 20: GEOS-Chem updates improve KORUS-AQ ozone simulation
Median vertical profiles
Observed
GEOS-Chem
old version 13.3
Ozone, ppb HO2, ppb NO, ppb
Altitude, km
Inclusion of nitrate photolysis (NO3- + hv → 0.5 NO2 + 0.5 HONO) corrects ozone background
Slowdown of HO2 aerosol uptake, including volatile chemical product (VCP) emissions corrects HO2 and increases ozone production in boundary layer
Yang et al.,. In prep.

## Slide 21: Evidence of very high residential use of volatile chemical products (VCPs) in Korea and China
Ethanol is common tracer of residential VCPs; very high in Korea and China
Methanol is highly correlated with ethanol – also used in VCPs?
These emissions are not in current inventories!
Including US-based residential VCP emission factors cannot match the China and Korea data
Beaudry et al., in prep.
Ethanol (ppb)
Methanol (ppb)
Methanol (ppb)
Methanol (ppb)

## Slide 22: GEOS-Chem simulates ozone network and sonde data with minimal bias
90th percentile MDA8 ozone
(circles = network sites, background = GEOS-Chem)
Seoul has broad maximum in May-August
High background confirmed by sondes
Colombi et al., in prep.
Mean of daily ozonesondes over Seoul, May-June 2016

## Slide 23: GEOS-Chem can also reproduce 2015-2019 ozone trend in Seoul
Maximum increase in spring due to NOx decrease under VOC-limited conditions
Summer is more likely to be NOx-limited
Colombi et al., in prep.

## Slide 24: Sensitivity of ozone in Korea to anthropogenic emissions
GEOS-Chem 90th percentile MDA8 ozone in May
(all emissions)
East Asian background
(zero emissions in domain)
Korea and China emissions make comparable contributions to ozone over Korea
Very high East Asian ozone background prevents meeting a 60 ppb standard
Colombi et al., in prep.
Background
+ ship emissions
Background
+ S. Korean emissions
Background
+ Chinese emissions

## Slide 25: Need global perspective on ozone background and human influence
Satellite observations of NO2 column, 1015 molecules cm-2
Ozone pollution transport by source continent (GEOS-Chem model)
Strong westerlies,
1-month ozone lifetime
N America
Europe
Asia

## Slide 26: Peroxyacetylnitrate (PAN) as driver of human influence on ozone background
NOx
HNO3
PAN
Asian
boundary
layer
PAN
Subsidence over E Pacific:
Large ozone production
PAN gNOx
U.S.
boundary
layer
E. Asia Pacific United States
acetaldehyde
(also methylglyoxal, acetone)
+ OH
peroxyacetyl radical
PAN
PAN lifetime: 1 h at 295K
1 month at 250K

## Slide 27: Evidence for the importance of PAN in intercontinental ozone pollution
Aircraft observations of Asian plumes transported over California
CO
O3
PAN
HNO3
May 5 plume at 6 km:
High CO and PAN,
no O3 enhancement
May 17 subsiding
plume at 2.5 km:
High CO and O3,
PAN gNOxgHNO3
Hudman et al. [2004]
NOx
NOx
HNO3
PAN
O3
CO

## Slide 28: IASI satellite observations of PAN over Pacific: large transpacific influence in spring
Spring has active photochemistry combined with strong westerly winds
Increasing pollution in Southeast Asia may also contribute
Zhai et al., in prep.

## Slide 29
Daily IASI PAN from Metop-A: day to day animation
Molec cm-2
Zhai et al., in prep.

## Slide 30: Rising PAN has implications for rising ozone background
molec cm-2
molec cm-2
MetopA
MetopB
MetopC
East China
Transport pathway
Zhai et al., in prep.

## Slide 31: Take-away messages
Ozone pollution is very high and increasing in Korea and China
High ozone reflects NOx and VOC emissions on top of a very high background
Increasing ozone over Korea is driven by declining domestic NOx emissions under VOC-limited conditions
The Korean air quality standard of 60 ppb cannot be met unless the East Asian background decreases
Importance of ozone background requires a global perspective on ozone pollution, including the complex role of PAN.

## Slide 33: Same basic mechanism for VOC oxidation but many branches
OH can also add to double bonds of unsaturated VOCs, producing hydroxyorganics
RO can also decompose or isomerize to produce a range of aldehydes, ketones, dicarbonyls…
NO can also add to produce organic nitrates
Oxidation product goes on to react with OH, adding functionality and making more ozone
RO2 can also
isomerize, or react with HO2 or RO2,
producing peroxides, epoxides,
alcohols,
carboxylic acids…

## Slide 34: 2015-2019 ozone increase in Korea
Colombi et al., in prep.
Meteorology-corrected ozone trend in Seoul
NOx emissions in S. Korea decreased by 20% from 2015 to 2019 while VOCs and PM stayed flat.
Sharpest ozone increase in spring is consistent with VOC-limited conditions, influence from China

## Slide 35: Peroxyacetylnitrate (PAN) as reservoir for intercontinental transport of NOx
VOC
acetaldehyde
(also methylglyoxal, acetone)
+ OH
peroxyacetyl radical
PAN
PAN lifetime: 1 h at 295K
1 month at 250K

## Slide 36
0 20 40 60 80 100 120 ppb
Europe AQS
(seasonal)
U.S. AQS
U.S. AQS
Preindustrial
ozone
background
Present-day ozone background at northern mid-latitudes
Europe AQS
S. Korea AQS
Ozone air quality standards (AQS) around the world
2008
2014
1997
China AQS
Canada AQS
Ozone AQS can be designed to protect against short-term effects (morbidity), long-term effects (mortality), vegetation
Standards tend to be aspirational or practical, with different levels of enforcement
Increasing epidemiological studies are revealing adverse effects at lower thresholds
Unlike for other pollutants, adverse effects of ozone occur at concentrations only marginally higher than background