## Slide 1: High spatiotemporal resolution trends of PM2.5 in East Asia inferred from the GOCI geostationary instrument, 2011-2020 Drew Pendergrass | GEMS Meeting September 8, 2023 with Daniel J. Jacob, Yujin Oak, Jhoon Kim, Jeewoo Lee, Seoyoung Lee, Shixian Zhai, and Hong Liao
Notes: Outline: We’ll start by talking about why care about particulate matter and why using satellites is appealing for modeling. Then we’ll describe the random forest algorithm and discuss its accuracy. Finally we’ll spend some time exploring the results and discussing what it tells us about particulate air quality in East Asia. The background are my modelled predictions for annual PM in Korea from 2015 to 2019.

## Slide 2: Previous work used GOCI 6x6 km2 AOD retrieval to infer daily PM2.5 in East Asia via a machine learning method
Pendergrass et al., 2022
GOCI PM2.5 v1.0 generated continuous PM2.5 fields using a random forest trained on AOD, surface PM2.5, and covariates.

## Slide 3: A new 2x2 km2 GOCI AOD retrieval enables sharper product: GOCI PM2.5 v2.0

## Slide 4: Data for training GOCI PM2.5 v2.0
Ground PM2.5 data
NIES (2011-20)
China MEE (2014-20) +
US Embassies (2011-20)
AirKorea PM2.5 (2015-20) +
Est. from PM10 (2011-20)
GOCI AOD and gap-filling information
Landcover and metadata
Day of year
Nation
Input vector
Target value y
24-hr average taken
at each site
Emissions and CTM monthly means
Meteorology
Population
Elevation
Land cover type
NDVI
Boundary level height
Sea level pressure
Relative humidity
Temperature
U winds
V winds

## Slide 5: v1.0 AOD gap filling: statistical interpolation + chemical transport model
IDW interp.
Gaspari-Cohn function
GEOS-Chem avgs.

## Slide 6: v2.0 AOD gap filling: separate random forest, use GEOS-Chem AOD as additional covariate
Separate RF fit
Yonsei U. retrieval
AOD for inferring PM2.5
3
2
1
0
Filled AOD
Retrieved AOD
Trained to predict AOD, using the same meteorology/land use used to train PM2.5 RFs.
Missingness data (same as v1) passed on to PM2.5 RF so that gap-filled data is weighted appropriately
Huge training set, so split by year. R2 ranges from 0.86-0.93
Notes: (follows new framework from Joel Schwartz’s group

## Slide 7
v2.0 extrapolation: in Korea, train on pre-2015 PM2.5 inferred from PM10 in Korea
PM2.5
Train on all covariates + AirKorea pollutants
(CO, SO2, NO2, PM10, O3, yellow dust events)
PM10
(2015)
Separate RF
(2015)
R2: 0.89

## Slide 8
1. Gapfill AOD
V2 workflow for continuous PM2.5 from AOD
AOD for inferring PM2.5
3
2
1
0
Filled AOD
2. PM10  PM2.5
3. Estimate PM2.5 for domain
Daily PM2.5 from March 2011
10
5
3
2
20
30
50
100
200
300
500
PM2.5 (µg m-3)

## Slide 9: Improved extrapolation into clean rural/mountainous regions (Kyushu case study)
8
10
12
14
16
18
20
22
GOCI PM2.5 v1
NIES sites
GOCI PM2.5 v2
2016 annual mean, Kyushu
Mountains
Coastal data missing due to ERALand; fixing now
Notes: Why this improvement? Better data, algorithm forced to perform better in rural areas by strongly increasing penalty. Not quite an apples-to-apples comparison, slightly different averaging periods.
Forcing better rural representation degrades representation in urban areas because only so much the cost function can do
Data ~10km from coasts missing due to higher-res reanalysis replay over land only (working on bug fix)

## Slide 10: Dramatic improvements in PM2.5 across three countries in study period
South Korea
Japan
Eastern China
National annual mean trends
Annual PM2.5 population exposures
Notes: In 2015, 55% of population in study domain are exposed to annual PM2.5 above the 50 ug/m3 level in 2015. This is down to 29% by 2019, with most improvement seen in China.

## Slide 11: Rapid but uneven improvements in PM2.5 across East Asia
15
10
5
0
-5
-10
-15
10
5
0
-5
-10
2012-20, annual trend
2015-20, annual trend
(relative to 2015)
(relative to 2015)
no recent trend in SMA; many rural areas

## Slide 12: Conclusions
GOCI PM2.5 v2.0 algorithm offers daily 24-h mean PM2.5 at 2km resolution from 2011-2020 for eastern China, South Korea, and Japan.
  Sharper separation of neighborhood-level pollution: ready for public health applications. Data will be free and publicly available online soon!
  Improved representation of clean areas relative to v1.0
PM2.5 concentrations predicted by the RF algorithm demonstrate dramatic improvements in pollution that slow by end of decade especially in rural areas
Improved dataset along with analysis of drivers will be released with paper soon – contact pendergrass@g.harvard.edu if interested.