## Slide 1: 14th GEMS Workshop Jeju, Sept 6-8. 2023
Harvard group
at GEMS meeting
Thanks to SAIT for supporting our GEMS research!

## Slide 2: Improved understanding of PM2.5 in Korea and China through integrated modeling and analysis of satellite, aircraft, and surface observations
Daniel Jacob
Samsung PM2.5 Strategic Research Program
Interim Year 4 Report
Two new papers since last report:
Dang, R., D.J. Jacob, S. Zhai, P. Coheur, L. Clarisse, M. Van Damme, D.C. Pendergrass, J.-S. Choi, J.-S. Park, Z. Liu, and H. Liao, Diagnosing the sensitivity of particulate nitrate to precursor emissions using satellite observations of ammonia and nitrogen dioxide, submitted to Geophys. Res. Lett., 2023.
Pendergrass, D.C., D. J. Jacob, H. Nesser, D.J. Varon, M. Sulprizio, K. Miyazaki, and K.W. Bowman, CHEEREIO 1.0: a versatile and user-friendly ensemble-based chemical data assimilation and emissions inversion platform for the GEOS-Chem chemical transport model, EGUsphere [preprint], https://doi.org/10.5194/egusphere-2023-616, 2023.
Also six presentations at GEMS Science Team meeting held on Sept 6-8 in Jeju
Ruijun Dang
Drew Pendergrass

## Slide 3: Using satellite observations of NH3 and NO2 to diagnose sensitivity of PM2.5 nitrate to emissions
IASI, 2017
OMI, 2017
NH3
Tropospheric NO2

## Slide 4: As SO2 and primary organic aerosol emissions have decreased, nitrate has emerged as a top problem for PM2.5 air quality
Organic
Sulfate
Nitrate
Ammonium
Chloride
Elemental
carbon
Li et al., 2019
PM2.5 composition in Beijing, 2014-2017
Seoul PM2.5 trend, 2015-2019 – increasing winter trend due to nitrate?
Pendergrass et al., 2022

## Slide 5: PM2.5 nitrate formation may be NOx-, NH3-, or VOC-sensitive
NH3
agriculture
vehicles
NO
fuel
NO2
HNO3
NH4+ + NO3-
PM2.5 nitrate
NO2: OMI, TROPOMI, GEMS
NH3: IASI, CrIS
OH, O3
hv
O3, peroxy
VOCs
fuel
volatile chemical compounds (VCPs)
vegetation
Can we use the NH3/NO2 ratio from satellite to diagnose sensitivity regime?
Test in GEOS-Chem model world

## Slide 6: Diagnosing PM2.5 nitrate formation sensitivities in GEOS-Chem
GEOS-Chem provides credible simulation of PM2.5 nitrate variability
Diagnose local model sensitivity S of monthly mean PM2.5 nitrate [NO3-]
to 20% decreases (Δ) of emissions (X≡ NH3, NOx, NMVOCs)
Dang et al., submitted

## Slide 7: Diagnosing PM2.5 nitrate sensitivities vs. ΩNH3/ΩNO2 and ΩNO2 in model world
Points show dominant sensitivities for 50-km model grid cells in China and S. Korea
(January 2017)
ΩNO2 diagnoses
NOx- vs. VOC-limited
oxidant regime
Location in (ΩNH3/ΩNO2, ΩNO2) space diagnoses dominant sensitivity
Dang et al., submitted
Ω denotes the tropospheric columns as would be observed from satellites

## Slide 8: Application to IASI (NH3) and OMI (NO2) satellite data
NH3-sensitive in Beijing;
mostly NOx-sensitive in North China Plain (but VOC-sensitive where NOx is very high)
mostly NH3- sensitive elsewhere, including in Korea
Dang et al., submitted
Satellite data indicate different sensitivity regimes for PM2.5 nitrate formation:

## Slide 9: CHEEREIO: an LETKF-based user-friendly inversion tool to infer emissions from satellite (and other) data
GEMS observations: NO2, formaldehyde, glyoxal, CO, ozone
IASI/CrIs observations: NH3
emissions of PM2.5 and ozone precursors
NOx VOCs NH3 CO
Transport
Non-linear chemistry
Chemical transport model (CTM): predict concentrations
from input emissions
Inversion:
infer emissions
from observed concentrations
LETKF = localized ensemble transform Kalman filter

## Slide 10: LETKF:
Time
Concentration
Ensemble of simulations
Observations
Information from observations
accumulates with time
Create ensemble of CTM simulations sampling uncertainty range of emissions
Assimilate observations, correct emissions including error characterization
Start with prior estimate of emissions
Emission estimates evolve with time
allows non-linear inversions without a model adjoint
can flexibly integrate all observations available
provides error characterization on results

## Slide 11: CHEEREIO is designed to allow non-expert users to flexibly apply LETKF to a wide range of observations for optimizing time-dependent emissions
Runtime operations
User configuration file:
Select satellite and other data
Select emissions to be optimized
Select domain and period
Select prior estimate, error parameters
Run CHEEREIO
https://cheereio.readthedocs.io/
Optimized high-resolution time-dependent emissions
Pendergrass et al., in press
All the software engineering is under the hood

## Slide 12: Demo weekly inversion of TROPOMI methane satellite data
TROPOMI data
posterior / prior methane emissions
0
1
2
3
4
5
CHEEREIO
2050
1850
1950
1750
XCH4, ppb
Pendergrass et al., in press

## Slide 13: Next step: apply CHEEREIO to GEMS+IASI satellite data over East Asia
GEMS: geostationary instrument
3.5x8 km2 pixels, hourly data
NO2, formaldehyde, glyoxal, ozone, CO
IASI: low Earth orbit instrument
12x12 km2 pixel, daily data
NH3
CHEEREIO
Optimized emissions
of NOx, VOCs, CO, NH3

## Slide 14: 1-slide summaries of GEMS meeting presentations …to be turned into papers acknowledging SAIT support

## Slide 15: Quantifying NOx point sources with Landsat and Sentinel-2 satellite observations of NO2 plumes
Detect plume over urban background
Resolve point sources 2 km apart
Resolve individual stacks
Detect down to 500 kg h-1
Daniel Varon et al., in prep.
Landsat and Sentinel-2 have ultra-blue (430-450 nm) bands sensitive to NO2
10-60 m pixel resolution offers unique capability to observe NO2 point sources
Apply to power plants in Saudi Arabia and US

## Slide 16: Improved mapping of PM2.5 over East Asia with GOCI geostationary data (2010-)
Drew Pendergrass et al., in prep.
Yonsei 2x2 km2 GOCI AOD product
daily 2x2 km2 PM2.5
Visible radiation
aerosol
optical
depth (AOD)
surface reflection
aerosol
AOD
gap-filling
random forest algorithm
trained with surface network data
Daily PM2.5 with 2x2 km2 resolution for eastern China, S. Korea, Japan

## Slide 17: Interpretation of the diurnal variation of NO2 observed by GEMS
GEMS and GEOS-Chem diurnal variations over Seoul (SMA) and Beijing (BTH)
Laura Yang et al., in prep.
summer
winter
Daytime chemical loss in summer, emission build-up in winter

## Slide 18: TROPOMI-corrected GEMS NO2 product
TROPOMI:
XT
GEMS:
XG + retrieval
parameters xG
Train ML model for
Δ(XG – XT) = f(xG)
Correct GEMS product:
XG – f(xG)
dense and precise
collocated data subset
full dataset
improve
retrievals
new product
mature product
Yujin Oak et al., in prep.
GEMS version 2.0 TROPOMI-corrected
X = NO2 tropospheric column
TROPOMI-corrected GEMS product combines precision of TROPOMI with density of GEMS
We will use this for inversions with CHEEREIO

## Slide 19: Origin of high free tropospheric ozone over Korea
GEMS observes high free tropospheric ozone over Korea, reproduced by GEOS-Chem; now investigating the source of this maximum
Pohang vertical profile
Nadia Colombi et al., in prep.
GEOS-Chem
Pressure, hPa
Ozone, ppb
Korea cannot meet its 60 ppb ozone air quality standard because of high concentrations in free troposphere (2-8 km altitude) subsiding to the surface
90
50
0
Ozone, ppb

## Slide 20: Evidence for high emissions of volatile chemical products (VCPs) in East Asia
Very high concentrations of ethanol and methanol in aircraft and surface observations over Seoul: implications for SOA and ozone formation
Ellie Beaudry et al., in prep.